## Slide 1: Simics/SystemC Hybrid Virtual Platform A Case Study
Asad Khan asad.u.khan@intel.com
Chris Wolf chris.m.wolf@intel.com

## Slide 2
Agenda
Simics/SystemC Hybrid Virtual Platform - explained
Simics and SystemC Integration
Performance Optimizations for the integrated model
Simulation Performance Metrics
Checkpointing
Summary

## Slide 3
Simics/SystemC Virtual Platform
IA Core/Uncore, interconnect bus fabric, PCH implemented within Simics
Security Acceleration Complex (AC) implemented using SystemC (SC)
Co-simulation
  Single thread simulation
  Simics controls the SystemC scheduler
Bridge integrates Simics and SystemC
  implements synchronization between the two schedulers
  queues any future SystemC events onto the Simics scheduler for callback
  provides downstream/upstream accesses to/from the SystemC side
  sends Interrupts to IA
SystemC AC module encapsulates AC SystemC Models & PCIe endpoint
Notes: Security Device model is an Intel internal IP implementing authentication, cipher and compression algorithms. This is controlled by a micro-engine. The models are developed using C/C++ and wrapped using SystemC for architectural use cases. This is multi-man years of work and that’s why the integration of these models with Simics for firmware and driver development for the acceleration complex.
Corresponding DML (Simics) models were developed for some use cases, but these models weren’t detailed enough to promote low-level firmware and driver development, or any of the pre-Silicon use cases.

## Slide 4: Bridge Functionality
Simics uses a time-slice model of simulation
  Each master assigned a time slice before it is preempted
  Memory/register accesses are blocking, completing in zero time
Asynchronous communication model between Simics/SystemC
  When inter-simulation accesses happen between Simics and SystemC
  Breaks the time-slice model of Simics
  Any future SystemC events (clock or sc_event) trigger future SystemC scheduling
Simics and SystemC are temporally coupled through the bridge
  Synchronizes Simics and SystemC times
  Posts any future events from SystemC to Simics event calendar
  Provides upstream/downstream access through interfaces to respective memory spaces
  Sends device interrupts from SystemC device model to Simics

## Slide 5
Performance Optimization – Simics/SystemC Platform
Problem Statement?
Context switches between Simics/SC are expensive for performance
  Context switches happen because of
    SC model clock ticks or due to scheduled events on SystemC calendar
    Polling of AC Profile registers in tight loops
    PCIe Configuration and MMIO accesses to the AC from IA – useful work
SystemC AC model is a clock based model
Solution
  Reduce context switch between Simics/SystemC
How?
  Downscaling of SystemC clock frequencies by increasing clock period
  Add fixed stall delay when AC profile registers are read
Notes: SystemC model is clock based due to its inner workings and how the models were originally developed. Again due to the complexity of the models, this restriction can’t be easily removed without significant modeling effort.

## Slide 6
Performance Optimizations – SC Clock Scaling
Performance gains of the order of 10000 obtained through clock-scaling compared to a non-scaled model for OS boot
Simics-SystemC co-simulation runs 3-5 times slower than wall-clock compared to 1-2 times slower for standalone Simics
Notes: Clock scaling obtained by multiplying the clock periods with a constant factor decreasing the clock frequency, and correspondingly decreasing the context switch between Simics and SystemC.

## Slide 7: Performance Optimizations – Polling Mode
Performance gains of 40-60% obtained for PCIe device setup and SW test execution with fixed stall cycles
Code running on IA (Simics) polls status registers on the SystemC side for status updates in tight polling loops
Due to clock-scaling, multiple polling events happen between SystemC clock ticks
No changes in SystemC subsystem between contiguous clock events
Reduce frequency of polling between clock ticks by adding stall time at poll
Notes: Stall times during poll essentially add a stall delay every time a poll register is read. This has the effect of increasing the polling period, thereby reducing polling frequency in between clock periods when there is no change in state of these status registers.

## Slide 8
Performance Optimizations – SC Code Refactoring
SystemC uses Processes for concurrency
  SC_THREAD() & SC_METHOD()
SC_METHOD() process run to completion like functions
SC_THREAD() process kept for the duration of the simulation through an infinite loop
  Halted in the middle of the process through wait statements which save the state of the thread on the stack
Problem
  SC_THREAD() processes are expensive for simulation performance due to context to be stored at the wait()
  A side effect is lack of support for checkpointing of SC_THREAD() because data on the stack is not accessible
Solution
  Replace SC_THREAD() processes w/ SC_METHOD() processes
Notes: We replaced all SC_THREAD() processes with SC_METHOD() processes from the SystemC model. A side-effect is replacement of trigger events of wait() statements with sc_event()s. Performance gains are illustrated through an example.

## Slide 9
Performance Results for SW Use Model (all times in seconds)
 | Boot Time | Setup Time w/o Stall | Setup Time w/ Stall | Test Time w/o Stall | Test Time w/ Stall
Poll Mode Driver |  |  |  |  | 
SC_THREAD() | 197 | 376 |  | 408 | 230
SC_METHOD() | 199 | 353 |  | 375 | 212
Interrupt Mode Driver |  |  |  |  | 
SC_THREAD() | 197 | 778 | 332 | 670 | 475
SC_METHOD() | 199 | 670 | 313 | 660 | 452
1st order performance improvement through clock scaling
2nd order Performance gains of 40-60% obtained for CPM setup and SW test execution with fixed stall cycles
3rd order performance gains of 3-15% through SystemC code refactoring
Notes: Interrupt mode driver is supposed to have a better response than the poll-mode driver. However this is not an apples to apples comparison, as the two-drivers came from different sources and did not have the same code-base.

## Slide 10: Simics-SystemC Performance Optimization2: Temporal Decoupling
Allocate execution time slice to SystemC through event scheduling
  Similar to Simics master scheduling
Run SystemC with “sc_start()” for a fraction of time slice duration
Don’t post SystemC events on Simics event Q for SystemC scheduling
  SystemC only scheduled through time slice
Simics and SystemC no more time synchronized
Sideeffects:
  Simics time runs ahead of SystemC time
    Aggregate time difference between Simics and SystemC keeps growing
  SystemC Interrupt scheduling will be impacted due to delayed interrupt response

## Slide 11
Simics-SystemC Performance Optimization2: Temporal Decoupling – Statistics
 | SystemC Time Slice sec | SystemC run time psec | SystemC Scale Factor | Fedora OS Boot Time
Temporal Coupling |  |  | 10000 | 19:00min
Temporal decoupling | .001 | 10000 | 100 | 17:50/19:00
 | .001 | 1000000 | 1 | 24:15
 | .001 | 1000000 | 10 | 21:45/28:30
 | .001 | 1000000 | 100 | 19:0/21:45
 | .001 | 100000 | 1 | 23:30
 | .001 | 100000 | 10 | 18:55
 | .001 | 100000 | 100 | 18:55
Through temporal decoupling, a much smaller scale factor (100) can yield to similar performance as with the temporally coupled case (scale factor of 10000)
Notes: SW with timeouts is the target. Originally some of these timeouts had to be increased because of scaling of the SystemC clocks. With temporal decoupling, any impacts on the SW should be reduced.

## Slide 12: Checkpointing – Saving TLM transactions
SystemC model uses Global memory manager for TLM generic payload (tlm_gp)
  Pointers for “tlm_gp” are passed around the model
  Only one value of each tlm_gp in the model – no copies.
Save transaction/extensions/data and corresponding pointers
Upon system Restore – do Globally
  Create new transaction, extensions
  Create Global transaction pointer STL map (old_tlm_gp_p, new_tlm_gp_p)
  Update tlm_gp fields
For each SystemC module
  Restore old tlm_gp pointers within modules
  Use STL map to find new pointer locations for tlm_gp with the restored data
Notes: Checkpointing saves the state of the platform for cases of interest. Platform can be restored from a saved checkpoint very quickly.
Saving the state of a SystemC model involves saving the event list along with the tlm_generic_payload values
Since tlm_generic_payload entries are passed within the model as pointers, a map of <old_p, new_p> is developed upon system restore. Old pointer values from this map are used to find the new pointers to restored tlm_generic_payload entries.
SCML registers saved
Green configuration parameters saved

## Slide 13
Checkpointing - Saving Payload Event Queues (PEQs)
SystemC TLM standard provides a mechanism to store future events tied to tlm_gp.
Events are stored in PEQs
Checkpoint updates made to TLM headers for PEQs
Save contents of the PEQ to Simics database - What is saved
  tlm_gp *s
  tlm_gp phase
  Future SystemC event trigger time
Upon Restore
  from the tlm_gp STL map, updated address (pointer) of the restored tlm_gp entries
  PEQ entry’s phase and schedule time
  Insert the PEQ in the time ordered list of events
  Calls “notify” on the event variable with the tlm_gp entry and time to reschedule the events

## Slide 14: Summary
A Simics/SystemC co-simualting virtual platform
Performance optimizations implemented to resolve performance bottlenecks for OS boot, firmware, driver, system validation and SW use cases.
2nd level optimization developed by temporally decoupling the two simulators.
SystemC save/restore capability developed for saving the entire state of the Platform through Simics checkpointing.
VP employed enabling SW shift left for 3 generations of the AC.